CATALOG IDENTIFICATION_______________________  DATE OF CATALOG___________________

Note:  Please reference your completed CRP Form to determine which selections are appropriate.

I.   SEAL USAGE IN CATALOGS

1. Pick the correct AMCA Seal: [check all that apply]

Air Performance

Sound and Air Performance

Efficiency Air Performance

Efficiency Sound and Air Performance

Fan Efficiency Grade (FEG) Air Performance

Fan Efficiency Grade (FEG) Sound and Air Performance

Fan Efficiency Grade (FEG)

2. FEG Seal Usage

All models FEG Certified.

Use AMCA Sound & Air Performance FEG Seal or AMCA Air Performance FEG Seal (whichever is applicable) with qualifying statement as usual.  No need to use AMCA Seal (blue & yellow) in addition, unless desired by Licensee.

Some models FEG Certified.

Use AMCA Sound & Air Performance Seal or AMCA Air Performance Seal (whichever is applicable) for models which are not AMCA Certified for FEG.  In addition, use AMCA Sound & Air Performance FEG Seal, AMCA Air Performance FEG Seal or generic FEG Seal (whichever is applicable) for models which are AMCA Certified for FEG.  See AMCA 211, Section 7.2.1 for additional statement requirements.

3. Placement of AMCA Seal: [check all that apply]

If the catalog contains all licensed products, the seal and qualifying statement shall be prominently displayed either on the cover or in the catalog.

If the catalog contains both licensed and unlicensed products, the AMCA Seal and qualifying statement shall not be shown on the outside cover.

II.   QUALIFYING STATEMENT ADJACENT TO THE SEAL

In catalogs containing ratings of licensed products, the following statement shall be printed prominently and immediately adjacent to the reproduction of the AMCA Certified Ratings Seal:

"(Licensee's name as shown on License Agreement) certifies that the (product description) shown herein is (or are) licensed to bear the AMCA Seal.  The ratings shown are based on tests and procedures performed in accordance with AMCA Publication 211 (and AMCA Publication 311 if sound is also certified) and comply with the requirements of the AMCA Certified Ratings Program."

In cases where some models within a product line are FEG Certified, but others are not, please provide the following statements in addition to the qualifying statement:

“The AMCA Certified Ratings Seal applies to air performance (and sound) for Models XXX only.”

“The AMCA Certified Ratings Seal applies to FEG for Models XXX only.”

III.  CATALOG IDENTIFICATION REQUIREMENTS

Catalogs containing performance ratings of licensed products shall have a catalog identification reference (e.g. Catalog No. XXX Rev. 1), and unabbreviated current catalog date, (e.g. November 2004) on the outside front or back cover.

Where ratings are on separate sheets or on loose leaf that may be removed from the cover, each sheet or loose leaf shall be identified and dated as above.

IV.  EFFICIENCY

The following statement shall be shown immediately adjacent to the efficiency ratings:

Efficiency ratings are fan static (or fan total) and include (or exclude) bearing and/or Power Transmission Losses.

V.  REQUIREMENTS FOR AIR PERFORMANCE

1.  Duct Statement (Installation Type Testing Method)

Installation Method [this is different from the rating method; see test report for installation method; check one]

One of the following statements shall be shown immediately adjacent to the rating tables, graphs and charts:

A		Performance certified is for installation type A – Free inlet, Free outlet.

B		Performance certified is for installation type B – Free inlet, Ducted outlet.

C		Performance certified is for installation type C – Ducted inlet, Free outlet.

D		Performance certified is for installation type D – Ducted inlet, Ducted outlet.

A & C	Performance certified is for installation type A & C – Free or ducted inlet, Free outlet.

B & D	Performance certified is for installation type B & D – Free or ducted inlet, Ducted outlet.

2.  Rating Method (see last page of Publication 211 to determine rating method) [check one]

Determine the rating method and then check the appropriate statements to be used.  The statements shall be shown immediately adjacent to the rating tables, graphs or charts.

A. 		Rating Method "A" (Constant Speed, Transmission Loss Not Included)

B. 		Rating Method "B" (Constant Speed, Transmission Losses Included)

C. 		Rating Method "C" (As Run Speed, Transmission Losses Included, Low Slip Motor)

D. 		Rating Method "D" (Direct Drive, Constant Speed, Low Slip Motor)

E. 		Rating Method "E" (Direct Drive, As Run Speed, Low Slip Motor)

F. 		Rating Method "F" (Direct Drive, As Run Speed, High Slip Motor)

The performance ratings for each model number shall include:

Airflow rate – Rating Methods A, B, C, D, E, F

Static pressure and/or total pressure - Rating Methods A, B, C, D, E

Static pressure – Rating Method F

Fan input power - Rating Methods A, B

Maximum fan input power over the range catalogued, or fan input power at the stated duty – Rating Method C

Maximum fan input power over the range catalogued, or fan input power at the stated duty, or maximum motor input watts, voltage and frequency over the range catalogued, or motor input watts, voltage, and frequency at the state duty. – Rating Methods D, E

Maximum motor input watts, voltage and frequency over the range catalogued, or motor input watts, voltage, and frequency at the stated duty (optional if less than 500 watts). – Rating Method F

Impeller speed - Rating Methods A, B, D

Actual impeller speed at each point of ratings or a nominal speed. – Rating Methods C, E F

Inlet air density (if other than standard air) – Rating Methods A, B, C, D, E, F

Fan static and/or fan total efficiency (optional) – Rating Methods A, B, C, D, E, F

Required Statements:

Power rating (watts, kW or BHP) does not include transmission losses. – Rating Method A

Power rating (watts, kW, or BHP) includes transmission losses. – Rating Method B

Speed (RPM or RPS) shown is nominal.  Performance is based on actual speed of test.  Use this statement only when nominal speed is catalogued. – Rating Methods C, E, F

Performance ratings do not include the effects of appurtenances (accessories). – Rating Methods A, B, C, D, E, F

Or

Performance ratings include the effects of [list appurtenances here]. – Rating Methods A, B, C, D, E, F

# Text boxes

CHECKLIST: CENTRIFUGAL, MIXED FLOW, AXIAL, PROPELLER, PRV, ERV AIR PERFORMANCE CATALOGS