CATALOG IDENTIFICATION_______________________  DATE OF CATALOG______________________

Note:  Please reference your completed CRP Form to determine which selections are appropriate.

I.   SEAL USAGE IN CATALOGS

A. Pick the Correct Seal: [check all that apply]

Air Leakage

B. Placement of Seal: [check all that apply]

If the catalog contains all licensed products, the seal and qualifying statement shall be prominently displayed either on the cover or in the catalog.

If the catalog contains both licensed and unlicensed products, the AMCA Seal and qualifying statement shall not be shown on the outside cover.

II.   QUALIFYING STATEMENT ADJACENT TO THE SEAL

In catalogs containing ratings of licensed products, the following statement shall be printed prominently and immediately adjacent to the reproduction of the AMCA Certified Ratings Seal:

“(Licensee's name as shown on License Agreement) certifies that the (product description) shown herein is (or are) licensed to bear the AMCA Seal.  The ratings shown are based on tests and procedures performed in accordance with AMCA Publication 511 and comply with the requirements of the AMCA Certified Ratings Program.”

III.  CATALOG IDENTIFICATION REQUIREMENTS

Catalogs containing performance ratings of licensed products shall have a catalog identification reference (e.g. Catalog No. XXX Rev. 1), and unabbreviated current catalog date, (e.g. November 2004) on the outside front or back cover.

Where ratings are on separate sheets or on loose leaf that may be removed from the cover, each sheet or loose leaf shall be identified and dated as above.

V.  ADDITIONAL REQUIREMENTS

A. Air Leakage Ratings

Published rating of air leakage performance shall be a statement of the maximum tested air leakage flow rate for each gauge at 3.75 kPa (15 in.wg) ∆Ps in m3/hr per 9.29 m2 (cfm per 100 ft2) of duct wall surface area at standard air density.

Published data shall state the length, gauge and diameter of the test sample.

Published air leakage data shall state that air leakage is based on operation between 10oC – 40oC (50oF – 104oF).

Published data shall clearly identify the certified product.

Each gauge of spiral duct published in a catalog must be certified.

# Text boxes

CHECKLIST:  SPIRAL DUCT CATALOGS